## Slide 1: Generation of Tunable, Coherent Terahertz Radiation Through Molecular Modulation
J.J. Weber and D. D. Yavuz
University of Wisconsin - Madison
This work was funded by the NSF and UW-Madison
Optical Modulator
We have constructed a broadband optical modulator with a modulation frequency of 89 THz. Our modulator is based on continuous-wave stimulated Raman scattering in molecular hydrogen inside a high finesse cavity.
785 nm
1064 nm Raman Pump
1555 nm Raman Stokes
785 nm
750 nm
823 nm
hνmod
λPump
1064nm
σ+
λStokes
1555nm
σ -
λSideband
750nm
σ+
λMixing
785nm
σ -
Molecular Modulation
Using high intensity fields, we build up a coherent state by driving a rotational Raman transition in molecular hydrogen. The driving lasers, the pump and the Stokes, build up the molecular coherence that is used to modulate an independent mixing laser. The generated sidebands are shifted by the modulation frequency, νmod, which is set by the frequency of the Raman transition.
|
A 1064 nm external cavity diode laser is amplified by a Ytterbium fiber amplifier. The resulting 30W beam is locked to a H2-filled high finesse optical cavity (finesse ~ 20,000) via a Pound–Drever-Hall locking circuit. This beam serves as the Raman pump beam. The Raman Stokes beam is generated through Raman lasing inside the cavity. The cavity mirrors are reflective at the pump and at the Stokes wavelengths. A second external cavity diode laser is then used to generate an independent mixing beam, which is modulated by the coherently rotating molecules in the cavity. This beam is not resonant with the cavity and thus is modulated in a single pass.
Experiment
Towards Arbitrary Optical Waveform Generation
Unlike other optical modulation techniques, molecular modulation has broadband modulation capabilities. With the appropriate optics, our modulator would be capable of modulating any optical frequency from 200 nm to 10 μm. The plot shows the theoretical efficiency of incident-to-sideband power conversion.
Wavelength (nm)
Intensity
Intensity
Wavelength (nm)
YFA – Ytterbium Fiber Amplifier EOM – Electro-Optic Modulator ECDL – External Cavity Diode Laser PBS – Polarizing Beam Splitter λ/2 – Half-Wave Plate
GS – Glass Slide PD – Photodiode MML – Mode-Matching Lens HFC – High Finesse Cavity
Conversion Efficiency
Wavelength (μm)
0.1
1
10
10-8
10-7
10-6
10-5
10-4
The curves represent the conversion efficiencies for different pressures of H2 inside the cavity. The solid red curve is 0.33 atm and the dotted green curve is 0.08 atm.
Wavelength (μm)
Intensity (arb. units)
Initial Ti:sapphire Spectrum
First Order Sidebands
Second Order Sidebands
Third Order Sidebands
Infrared
Visible
Ultraviolet
+
+
+
Electric Field
Time
or
Electric Field
Time
or
0.29 fs
With its broadband capabilities, a molecular modulator would be able to modulate the already broad output of a Ti:sapphire laser. The resulting spectrum would span the full optical region and would contain a few million CW Fourier components. Such a broad, coherent spectrum could be used to generate arbitrary optical waveforms with sub-femtosecond resolution.
Include efficiency to show difficulty
Include experimental stuff
Show efficiency as a function of …
Change vibrational levels, wavelengths
1555nm ECDL
– Raman Stokes
GS
To Detector
Er FA
To Locking Circuit
PD
1064nm ECDL
– Raman Pump
MML
D2-Filled HFC
GS
To Locking Circuit
EOM
PD
PBS
λ/2
785 nm ECDL – Mixing
Yb FA
MML
EOM
Prism
We introduce and numerically model an approach for generating coherent terahertz radiation. Our method is based on our experimental work with high frequency (10-100 THz) continuous-wave light modulation. We use continuous-wave stimulated Raman scattering inside a high-finesse cavity to modulate light at molecular frequencies. Our simulations demonstrate how this approach could be expanded to generate radiation outside of the optical range. An infrared mixing beam from a semiconductor diode laser could be frequency down-shifted by the molecular modulator in order to generate radiation in the terahertz region of the spectrum. The generated radiation would be easily tunable, as a tuning range of a few tens of nanometers in the diode laser would allow for generation of radiation spanning the entire terahertz region (1-10 THz). We explore the efficiency of this generation using numerical simulations with experimentally available parameters.
Only two outputs
New MatLab
output
Four-wave mixing
THz wavelengths
Challenges with diverging beam, transparency